## Slide 1: Cyber Security For Civil Engineering
Lecture 1
Thiago Alves
Ph.D. Student at the University of Alabama in Huntsville

## Slide 2: Who am I?
Ph.D. Student at the University of Alabama in Huntsville
SCADA Cyber Security Researcher at the Center for Cybersecurity Research and Education (CCRE)
Creator of the OpenPLC Project: www.openplcproject.com – The first fully open source Programmable Logic Controller

## Slide 3: What is Cyber Security?
Cyber security is the body of technologies, processes and practices designed to protect computers, programs and data from attack, damage or unauthorized access.
Notes: When a computer is embedded in a system, we usually call it CONTROLLER

## Slide 4: What is a Computer?
Notes: When a computer is embedded in a system, we usually call it CONTROLLER

## Slide 5: Dam Control and Monitoring
Notes: Are there computers here?
Hydraulic drives, gate controls, water level monitoring, etc

## Slide 6: Substation
Notes: Are there computers here?
Situational Awareness
Control -> Open/Close breakers

## Slide 7: Water Distribution
Notes: Are there computers here?
Hydraulic drives, gate controls, water level monitoring, etc

## Slide 8: Oil/Gas Distribution
Notes: Are there computers here?
Monitor Pressure
Route Product
Billing

## Slide 9: Petrochemical
Notes: Are there computers here?
Safety
Storage
Distillation Tower

## Slide 10: The set of computers, networked data communications and graphical user interfaces that monitors and control industrial processes is called SCADA

## Slide 11: What Is SCADA?
Supervisory Control And Data Acquisition
Notes: When controllers are applied to processes like shown before, the system is usually called SCADA

## Slide 12: What Is SCADA?
Supervisory Control And Data Acquisition
Huh?!

## Slide 13: What Is SCADA?
Supervisory Control And Data Acquisition
Supervisory | Control | Data Acquisition
Supervisor synonyms Manager Overseer Administrator | Change current state of process Open close breakers, switches, valves, etc. | Situational Awareness Monitoring

## Slide 14: SCADA Architecture
Physical System
(sensors and actuators)
Wired or Wireless Connection
Programmable Logic Controller (PLC)
Enterprise Network / Internet
Human-Machine Interface

## Slide 15: Physical System
Physical structure for the process
Embedded sensors that measure quantities such as pressure, temperature, flow, or density
Embedded actuators to control mechanisms such as solenoids, valves, or gates

## Slide 16: Wired (or wireless) Connection
Sends sensor signals to the controller
Sends controller commands to the actuators
Electrical communication between the controller and its physical interfaces

## Slide 17: Programmable Logic Controller
Digital Computer used on Automation
Input modules read data from sensors
User program decides what to do based on the input data
Output modules control actuators on the physical system

## Slide 18: Enterprise Network / Internet
Allows data exchange between the Programmable Logic Controllers and other computers
Enables supervisory software to query information from the plant
Communication follows a set of rules called Protocol
Output modules control actuators on the physical system

## Slide 19: Human Machine Interface
Graphical screens that consists of buttons, alarms, reports and trends about the process
Manages the physical process data
Provides a mechanism for user interaction and control

## Slide 20: Live Demo
Water Temperature Control

## Slide 21: Types of Harm
Interruption
Interception
Modification
Injection

## Slide 22: C-I-A Triad
Confidentiality
Integrity
Availability

## Slide 23: Confidentiality
Confidentiality is roughly equivalent to privacy. Measures undertaken to ensure confidentiality are designed to prevent sensitive information from reaching the wrong people, while making sure that the right people can in fact get it.
Notes: Discuss examples where confidentiality would and would not be important.
Not important: Water level on a water storage tank.
Important: Password to the gate controls on a penitentiary

## Slide 24: Integrity
Integrity involves maintaining the consistency, accuracy, and trustworthiness of data over its entire life cycle. Data must not be changed in transit, and steps must be taken to ensure that data cannot be altered by unauthorized people.
Notes: Discuss examples where integrity would and would not be important.
Not important: Bathroom lights control (questionable)
Important: Flood gate controls on a dam

## Slide 25: Availability
Availability means that the computing systems used to store and process the data, the security controls used to protect it, and the communication channels used to access it must be functioning correctly. High availability systems aim to remain available at all times, preventing service disruptions due to power outages, hardware failures, and system upgrades.
Notes: Discuss examples where availability would and would not be important.
Not important: None
Important: All